## Slide 1: IVR Assignment

## Slide 2: A - Robot Vision - Joint State Estimation
Method:
1. To find Joint angles, we used method:
      a. Use formula to find the angle between two vector: arccos( (v1.v2) / |v1| x |v2| )
      b. Find the sign(+/-) with rotation vector and vectors of two links of the joints sign = signOf ( (v1 x v2). vector_rotation )
      3. To find Joint velocity, we used method:
      a. Joint velocity = current joint angle –
      previous joint angle
Results:
1. position of joints result:
Work well in dark environment
2. Joint angles result: (average error)
    [0.023,0.027,0.026,0.014]
    3. Joint velocity result: (average error):
    [0.727, 0.902, 1.24]

## Slide 3: A - Robot Vision - Target Identification/Detection
Method:
To find position of joints, we used method:
      a. Convert RGB graph to HSV
      b. Detect joint with range of h and s and
      peak value of v
To Detect target we used two methods:
a. extract targets from xy-image and xz-image
b. use cv2.findContours in OpenCV to find the edge of the target
c. we used two method to distinguish between valid and invalid target:
A. SVM classifier
1.We constructed a SVM classifier and train it by adding train pictures.
2. Classify the extracted target by the trained SVM classifier
B. by pixel
1. By extract the features of target (here we extract difference between white and black)
Results:
1. Accuracy of position of joints:
    a. Accuracy of SVM classifier:
    1. The accuracy of SVM classifier is very low (56.4%) compare the other method, and to train the data, the whole process is very slow at same time.
    2. The
    b. Accuracy of detect by pixels
            The accuracy of this method is way more higher (about 100%) at this task, however if the target change, it will be very
            hard to detect.

## Slide 4: B - Robot Control - Inverse Kinematics Velocity Control
Experiments/results:
Velocity control:
a. Jacobian:
Since the axis of rotation in each joint change in 3D dimension, to calculate the Jacobian in geometrically, we should calculate the rotation axis for each joint by doing:
We begin with the joint close to the base and apply rotation matrix about current joint to the rest of rotation axis.
Since the rotation axis could be neither x, y or z, we should apply Rodrigues’ rotation formula
b. Inverse kinematics:
1. Calculate current position and error in position in task space
2. Calculate Jacobian:
a. If the Jacobian is low rank then use the transpose
b. Otherwise use pseudo-inverse
3. Apply inverted Jacobian on the position error in task space to get qdot

## Slide 5: B - Robot Control - Gravity Compensated Torque Control
Experiments
To calculate the torque for gravity, we use the method:
1. Calculate
results
To calculate the torque

## Slide 6: C - Open Challenge
Open Challenge Details/Explanation